# 2944K LABVISION

*Model views may not represent exact model purchased

TABLE OF CONTENTS

PAGE

REVISIONS TABLE…………………………………………………………………………………………………………………….…………………..……….………..……….…………………………………………..………………………………3

ASSEMBLY COMPONENTS…………………………………………………………………………………………………………………….…………………..……….……….…………….…………………………………………3

FILLER ASSEMBLY…………………………………………………………………………….…………………..……….…..……….…………….…………………………………………………………………………………………………………4

BACK ASSEMBLY………………………………………………………………………………………………….…………………..……….…………………………..……….…………….…………………………………………………………………4

LEG ASSEMBLY………………………………………………………………….…………………..……….…..……….………….….……………………………………………………………….………………………………………………………………5

APRON ASSEMBLY…………………………………………………………………………………………………………………….…………………………………..…………………………………………………..…………………………………5

APRON BRACKET…………………………………………………………………………………………….…………………..……….……………………………..……….…………………………………………………………………………………6

TOP ASSEMBLY……………………………………………………………………………………………….………….………………………………..……………………………………...….…………….……………………………………….…………….7

SINK ASSEMBLY…………………………………………………………………………………………………………………….…………………..…….….……………………….…………………………..……………..…………………………………7

FIXTURE ASSEMBLY…………………………………………………………………………………………………….………..………….…………………..……….…………………………………………………………………………………7

BASE MOULDING ASSEMBLY……………………………………………………………………………………………….………….……………………………..……………….………….………………….…………….8

PULL ASSEMBLY……………………………………………………………………………………………….………….………………………………..…………………………………..………….………………………………………….…………….8

ASSEMBLY COMPONENTS

| ITEMS INCLUDED | PART # |  | PART # |
| --- | --- | --- | --- |
| ASSEMBLY INSTRUCTIONS |  | 4-BOLTS,3/8-16X2" HEX HEAD | 100377 |
| 16-SHELF CLIPS | 100027 | 6-WASHERS, 5/16 FLAT ZINC PLATED | 100451 |
| 13.5 FT RUBBER BASE | 100283 | 4-NUTS 3/8X16 HEX ZINC | 100621 |
| 1-LEG LEVELER | 100079 | 12-SCREWS, #8X3/4 PHIL TRUS HD | 100649 |
| 2-CARRIAGE BOLTS, 5/16X2-3/4 | 100381 | 12-SCREWS, #8X1-1/4 WASHER HEAD | 100478 |
| 6-SCREWS, #10X1-1/2 PHIL TRUSS HD | 100495 | 1 - APRON TO APRON BRACKET | 100376 |
| 4-SS CORNERS | 100057 | 2 - APRON TO CABINET BRACKET | 100972 |
| 16-SS #6x1/2 PTH SCREW | 100064 | 2-NUT, 5/16X18 | 100044 |
| 1-OUTLET/STAINER EPOXY | 100055 | PHENOLIC TOP CARE INSTRUCTIONS |  |
| 1-PLASTIC TRAP | 100056 | 2-ELECTRICAL BOX | 100033 |
| 1-SINK STOPPER | 100112 | 2-GFI | 100034 |
| 1-SILICONE | 100711 | 8 - #6X 1/2" PPH SCREWS | 100475 |
| 1-LEG BOOT | 100076 | 1-HARDWARE BOX |  |
| 2-COAT HOOKS | 207663 | 2 FIXTURES,L65-WSA-DIV | 100074 |
| 1 EPOXY SINK,L3 | 100691 | 1-PHENOLIC TOP | 213597 |
| 1 FILLER PANEL 35X18 | BF3518KRCCG | 1-LEG, WING, 36 | L36-W |
| 1-APRON,4.5X36.81,RIGHT | 214001 | 1-APRON,4.5X36.81,LEFT | 214000 |
| 4-SHELF, ADJ 14 X 22.19 | 200397-2218 | 1-FILLER PANEL 35X66 | 212676 |

REV	                                                 DESCRIPTION			                  DATE      INITIAL

| --- | Original Created | 5-14-09 | NAM |
| --- | --- | --- | --- |

Assembly Instructions for

2944K LABVISION

Items not included but needed for assembly:

- Screwdriver with phillips bit

- 1/8” drill bit

- 1/2”and 9/16” wrenches

- Tape measure

- Level

- Contact Cement

- Liquid Nails or Silicone adhesive

Inspect all components for shipping damage.

Instructions:

- Position 2-24” base cabinets in desired location making sure door hinges are on the outside.

- Place 18” plywood panel between cabinets. Drill pilot hole thru panel into cleat.  Fasten with the 6 - #10 x 1 ½” decorative Phillips truss head screws.

- Place the 66” plywood panel on the backside of the cabinets. Fasten the back of the cabinets with the 12 #8 x 1 ¼” sq. drive washer head screws.

- Attach the apron-to-apron bracket to the L-36 leg using the 5/16” x 2 ¾” bolts. Make sure the bracket is positioned on the leg, with the ¾” spacing to the center hole, toward the top of the leg.

- Position leg with the steel bracket at the end of the aprons and attach using the 8 - #8 x ¾” truss head screws.

Figure 5A

Figure 5B

- Stand apron assembly up and slide up to cabinet back.

- While holding apron flush with cabinet top and 1/4” in from the sides, attach cabinet bracket to the back of cabinet with the 3/8”x 1 ½” hex head bolts.  Repeat on opposite side.

Figure 7A

Figure 7B

- With level, adjust leg leveler until entire frame is level with the cabinet.

- Apply a bead of silicone adhesive caulk around perimeter of frame and cabinet.  Set the epoxy top on the frame and cabinet, centering top on the frame for proper overhang.  Do not apply adhesive to the filler panels, doing so will prevent utility connections later. Let dry for 12 – 24 hours.

- Clean the top with water only making sure sink area is clean and dry.  Apply bead of silicone around the inside lip of sink opening and set sink in place. Let dry for 12 – 24 hours.

- Mount fixtures into place.

- Cut the rubber base molding to fit all sides of the workstation and attach using contact cement. After molding is in place, use the #6 x ½” SS screws to screw stainless steel corner brackets on each corner over the base molding.

- Reverse Door pulls as shown below.

- All water, electrical and gas connections should be performed by a trained professional.