PLAIN APRON TABLES

ASSEMBLY INSTRUCTIONS

*Model views may not represent exact model purchased

TABLE OF CONTENTS

ASSEMBLY COMPONENTS_______________________________________3

APRON TO LEG ATTACHMENT___________________________________4

LEG ASSEMBLY_________________________________________________5

LEG BRACES & STRETCHERS_____________________________________6

ASSEMBLY COMPONENTS

| ITEMS INCLUDED | PART # |  | PART# |
| --- | --- | --- | --- |
| 1-LEG KIT,TABLE |  | 1-APRON ASSY,TABLE |  |
| 1-TOP,TABLE |  | BOX,TABLES |  |
| 1--SCREW,#12.00X1 1/2 | 100062 | 8-SCREW,7MMX90MM | 227578 |
|  |  | OPTION FOR LEG BRACES |  |
| 4-SCREW,7MMX50MM, | 228564 |  |  |
| OPTION FOR STRETCHERS |  |  |  |

REV					DESCRIPTION		   DATE

| --- | Original Created | 5-15-09 | NAM |
| --- | --- | --- | --- |

# Assembly Instructions for

# Tables

Items not included but needed for assembly:

- ½” wrench

Instructions:

- Lay the table on the floor with the apron side up. (Be sure to lay the table on a clean surface so you don’t damage the tabletop.)

- Take each of the table legs and insert the stud bolt through the hole in the steel corner brace.

- Apply a lock washer and a 5/16” nut onto each stud bolt. Tighten each nut using a minimum of 12 foot-pounds but not exceeding 17 foot-pounds of torque.

- Slide leg boots onto the legs with the flared end toward the bottom of the leg.

- Screw leg levelers into t-nut in the bottom of the leg.

- Turn the table over so the top is up. Set your table in place and adjust the leg levelers to level the table.

- Slide the leg boot down to the floor.

- NOTE: TABLES WITH LEG BRACES AND STRETCHERS SEE

FIGURE 8A.

FIGURE 8A

- Attach  leg braces with: (SCREW,7MMX90MM,CONN,ALLENHEAD,BLACK) Provided

- Attach  stretcher with: (SCREW,7MMX50MM,CONN,ALLENHEAD,BLACK) Provided

# Text boxes

Stretcher

Leg Brace